## Slide 1: Lecture 5 Frequency and Spatial Domain Filters
ECE 1390/2390
Learning Objectives:
Frequency domain filtering
Window-method for FIR design

## Slide 2
DFT
Low spatial frequencies
High spatial frequencies
Image Resolution
1000 x 1000 [15cm x 10cm]
= 0.15 mm/pixel in X-direction
= 0.10 mm/pixel in Y-direction
Sample Rate
1/0.15 pixel/mm = 6.7 pixel/mm
1/0.10 pixel/mm = 10.0 pixel/mm
Nyquist Spatial Frequency
3.3 pixel/mm = 3.3 mm-1
5.0 pixel/mm = 5.0 mm-1

## Slide 3
DFT
iDFT
Low frequency mask

## Slide 4
DFT
iDFT
Low frequency mask

## Slide 5
DFT
iDFT
High frequency mask

## Slide 6: Butterworth
Corner frequency

## Slide 8: FIR design
Ideal filter
Realized filter

## Slide 9: FIR design
Ideal filter
Realized filter

## Slide 10: FIR design
Ideal filter
Realized filter
Parseval’s Theorem

## Slide 11: Window method for FIR design
= [k]
A= W(w)
Ideal filter
Time domain window

## Slide 12: Window method for FIR design

## Slide 13
Low-pass
High-pass
Band-pass
Notch

## Slide 14: Window method for FIR design
A= W(w)
a= ad(k)
W(w)

## Slide 15: Window method for FIR design
A= W(w)
a= ad(k)
W(w)

## Slide 16
Blackman
Hamming
Main-lobe width  transition bandwidth
Side-lobes  ripple in pass/stop band

## Slide 17
Main-lobe width  transition bandwidth
Side-lobes  ripple in pass/stop band

## Slide 18
2D FIR filtering
homogenous sampling

## Slide 19
Gaussian filter
FIR ideal LPF
FIR ideal HPF

## Slide 20: Window method for FIR design
A= W(w)
a= ad(k)
W(w)

## Slide 21: Window method for FIR design
a= ad(k)
“T” – temporal sampling interval  “voxel size”
”F” – temporal frequency (s-1)  spatial frequency (cm-1)
“w” – frequency in radians/s  same definition
Images are typically a lot fewer samples than time (e.g. 1024x1024 vs #time-points)
Larger filter kernels will have more edge effects (edges on all 4 sides of an image)
Zero-padding needed