## Slide 1: Lecture 12 Camera Calibration
Lecture 12 Camera Calibration
Lecture 12 Camera Calibration
Lecture 12 Camera Calibration
ECE 1390/2390

## Slide 2: Syllabus
Week | Date | Topic | In class work | Due date
8 | 10/14/2024 | FALL Break [No Class] |  | 
 | 10/16/2024 | Camera Calibration | Python problems (HW5) | Due 10/23
9 | 10/21/2024 | Depth estimation | Group Project work | 
 | 10/23/2024 | 3D Reconstruction and Pose estimation | Python problems (HW6) | Due 10/30
10 | 10/28/2024 | Haar Cascade Classifiers | Python problems (HW7) | Due 11/4
 | 10/30/2024 | HOG and Custom Detectors | Project updates | 
11 | 11/4/2024 | Object Tracking | Project updates | 
 | 11/6/2024 | OCR Text Detection | Python problems (HW8) | Due 11/13
12 | 11/11/2024 | MediaPipe/SLAM | Group Project work | 
 | 11/13/2024 | OpenCV DNN | Python problems (HW9) | Due 11/20
13 | 11/18/2024 | Super Resolution | Python problems (HW10) | Due 12/4
 | 11/20/2024 | Image compression | Python problems | 
14 | 11/25/2024 | Thanksgiving recess |  | 
 | 11/27/2024 | Thanksgiving recess |  | 
15 | 12/2/2024 | Group Project work | Group Project work | 
 | 12/4/2024 | Group Project work | Group Project work | Final project commit
16 | 12/9/2024 | Final Projects | Project presentations | Final group ratings

## Slide 3: Camera Calibration
CCD Grid
Ideal camera
Real camera
Offset of CCD center
from optical axis
X/Y CCD grid skew

## Slide 4: Camera Calibration

## Slide 5: Fourier Optics
=
=
Solving for the spherical wave propagation at point (x,y)
Free-space propagation of the light wave is a Fourier Transform
A confocal lens is an inverse Fourier Transform

## Slide 6: Fourier Optics
=
=
Higher spatial frequencies
Higher spatial frequencies
Low spatial frequencies
X
X
An ideal lens is a top-hat
low-pass-filter (multiplication)
in the spatial-frequency domain

## Slide 7: Fourier Optics
An ideal lens is a top-hat
low-pass-filter (multiplication)
in the spatial-frequency domain
f (focal length)
D (lens diameter)
= Index of refraction (air = 1)
Diffraction resolution
limit of a microscope

## Slide 8: Fourier Optics
=
=
An ideal lens is a top-hat
low-pass-filter (multiplication)
in the spatial-frequency domain
Iphoto)
Iphoto

## Slide 9: Fourier Optics
Spherical aberration
Negative aberration
Positive aberration
Ideal
Image from Wikipedia
Spherical aberration

## Slide 10: Fourier Optics
Wavelength dependent aberration
Image from Wikipedia
Chromatic aberration
V-I-B-G-Y-O-R

## Slide 11
Deconvolution (Wiener Filter)
Ng, Yiu-Ming Harry. “Correcting the Chromatic Aberration in Barrel Distortion of Endoscopic Images.” (2003).
Calibration Target
Photograph Raw
Corrected
Imperfect

## Slide 12: OpenCV Camera Calibration
Internal
  Focal
  Optical center
  Radial Distortion
External
  Orientation of target relative to camera

## Slide 13: Prospective-n-Point (PnP)
(x0,y0,0)
(x1,y1,0)
(x3,y3,0)
(x2,y2,0)
𝜽z
Y
X
Z
𝜽y
𝜽x
= *

## Slide 14: Prospective-n-Point (PnP)
= *
3D to 2D projection
Intrinsic Camera distortion

## Slide 15: Prospective-n-Point (PnP)
= *
3D to 2D projection
Intrinsic Camera distortion

## Slide 16: Prospective-n-Point (PnP)
= *
3D to 2D projection
Intrinsic Camera distortion
Differs per image
Same across images

## Slide 17: OpenCV Camera Calibration
img_points =[]
obj_points = []
for gray in images:
Step 1.
retval,corners = cv2.findChessBoardCorners(image=gray, patternSize=(10,8))
(optional)
corners = cv2.cornerSubPix(gray,corners,(11,11),(-1,-1),criteria)
(optional)
cv2.drawChessboardCorners
Step 2.
img_points.append(corners)
obj_points .append(real_coors)
Step 3.
ret, cameramtx, distcorr, rot, trans = cv2.calibrateCamera(obj_points,img_points,gray.shape[::-1],None,None)
These two arrays need to have corresponding points
Finds corners of checkerboard
Estimates sub-pixel position of corners
Camera (K) matrix
Distortion parameters
Estimated rotation/translation of each image

## Slide 18: OpenCV Camera Calibration
# shape of image needed to design undistortion filter
h,w = img.shape[:2]
# make camera matrix and valid ROI
newcameramtx, roi = cv2.getOptimalNewCameraMatrix(cameramtx, distcorr, (w,h), 1, (w,h))
# undistort image
dst = cv.undistort(img, mtx, dist, None, newcameramtx)
# crop the image
x,y,w,h = roi
dst = dst[y:y+h, x:x+w]
From previous steps